## Slide 1: Beacon Supplementary Information
IMAT5121
Main Coursework
2020/21

## Slide 2: Background
For Task 3 the robot is required to search and find the beacon, then travel to it until the distance between the robot and the beacon is less than 0.5 meters.
The simulators may have functionality for beacons, however some may not.
This guide will show you how the beacons will be implemented and used for the scope of this assignment.
If you are using a simulator different to the ones in this document then please see me as soon as possible.

## Slide 3: Background
Distance from beacon
Distance threshold – beacon can only be seen a certain distance away

## Slide 4: iRobot Create Toolbox Simulator
Camera = CameraSensorCreate(serPort);
% Task-2: homing into (reach) the beacon
Camera = CameraSensorCreate(serPort);
while (any(Camera))
Camera = CameraSensorCreate(serPort);
if any(Camera) && abs(Camera) > 0.05
turnAngle (serPort, .2, (Camera * 6));
end
SetDriveWheelsCreate(serPort, 0.4, 0.4);
pause (.1);
end
Create a Camera object using:
In a example:
(Full code example is on the assessment page)

## Slide 5: VREP
We use the distance calculation module from a object called “beacon” to the robot and read this distance through the remote API
If the distance is less than the threshold it is returned else -1 is returned

## Slide 6: VREP
# Start Beacon
res, self.distHandle = vrep.simxGetDistanceHandle(clientID, "beacon", vrep.simx_opmode_blocking)
res, distance = vrep.simxReadDistance(clientID, self.distHandle, vrep.simx_opmode_streaming)
res, self.beaconHandle = vrep.simxGetObjectHandle(clientID, 'beacon',vrep.simx_opmode_blocking)
Place this code with the object handles initialisation:

## Slide 7: VREP
def findBeacon(self):
# Maxiumum Distance the robot can sense the beacon
threshold = 7
# Get distance object
res, distance = vrep.simxReadDistance(clientID, self.distHandle, vrep.simx_opmode_buffer)
res, beaconPosition = vrep.simxGetObjectPosition(clientID, self.beaconHandle, -1 , vrep.simx_opmode_blocking)
# return distance or threshold
if distance >= threshold:
return -1
else:
return distance
Add this function after the module imports: